Group

Topic

3

Modbus RTU Slave for S7-200

| CPUs required for this tip |
| --- |
| CPU 210 ( | CPU 212 ( | CPU 214 ( | CPU 215 ( | CPU 216 ( | OTHER ( |

Overview

This program example includes a group of subroutines and interrupt routines which create a Modbus RTU slave using the Freeport functions of the S7-200. This program supports Modbus functions :

1	Read outputs (coils)

2	Read inputs (contacts)

3	Read holding registers (V memory)

4	Read input registers

5	Write single output

6	Write single holding register

15	Write multiple outputs

16 	Write multiple holding registers

Address 1			Address 2			Address 3			Address 4

Figure 41.1

Structure of Program

The Modbus protocol driver consists of a group of subroutines and interrupt routines which initialize and process the Modbus requests. There are two other networks neccesary in the user's main program. One network initializes the Modbus drivers on the first scan. The other network checks an M bit and processes a Modbus request if present. This second network should be placed near the end of the user's main program (just before the MEND) so that data is only changed at the end of the scan.

The subroutines and interrupts used are:

SBR  50		Initialize the Modbus RTU driver

SBR  51		Process a Modbus request and transmit the response

SBR  52		Process Modbus functions 1 and 2

SBR  53		Process Modbus functions 3 and 4

SBR  54		Process Modbus function 5

SBR  55		Process Modbus function 6

SBR  56		Process Modbus function 15

SBR  57		Process Modbus function 16

SBR  61		Generate error response two

SBR  62		Initialize CRC table

SBR  63		Calculate CRC

INT	  120	Handle quiet line timeout

INT	  121	Handle characters while waiting for a quiet line timeout

INT	  122	Receive first character (address field) of request

INT	  123	Receive remainder of request

INT	  124	Terminate request after quiet line timeout

INT	  125	Reset quiet line search after transmit complete

Description of the Program

This program allows one or more CPU 214s to be connected to a Modbus host. The program uses the CPU 214’s Freeport functions to implement the Modbus RTU protocol. Modbus RTU is a master-slave protocol; this means that a network configuration consists of one master (a host computer) and one or more slave devices. Each slave devices has a different address. The master sends a request to one of the slaves and then waits on the response from that slave. The slave will respond that the request was accepted or that there was an error. If the request was not received correctly, that is, there was a transmission error such as parity or a bad CRC (checksum), the slave will not respond, and the master must resend the request after waiting an appropriate time.

Modbus RTU is a binary protocol. The start of a message is denoted by a quiet time on the line for 3.5 byte time at the current baud rate. The end of the message is also denoted by the same quiet time on the line. Since the quiet line time is a multiple of character times, it will vary depending on the baud rate. The program described below sets the quiet line time to a value corresponding to 9600 baud. If the baud rate is changed, the quiet line time must also be changed. This is described in SBR 50.

Modbus RTU protocol transmits data in 8 bit binary characters. Each character also includes one start bit, one or two stop bits (the CPU 214 provides one stop bit) and an optional parity bit. The program described below sets the CPU 214 for 9600 baud with even parity. This may be changed by modifying the port setup in SBR 50.

Modbus RTU protocol uses a CRC (Cyclical Redundancy Check) to provide error detection. This application utilizes a table of CRC values to speed the calculation of the CRC when checking a received message and transmitting the response. This CRC table is generated in upper V memory during the initialization of the Modbus driver and requires about 700 milliseconds. This will occur on the first scan only.

Subroutines to support Modbus functions 1, 2, 3, 4, 5, 6, 15 and 16 are provided. If a particular master does not utilize all of these functions, they may be removed to provide more program space for the user program. To remove a function, remove the supporting subroutine and the call to that subroutine. The calls are all in SBR 51.

The functions supported via subroutines are:

1	Read single/multiple coil (output) status

Returns on/off status of any number of outputs (Q). The maximum number of

outputs may be specified by the user (see below).

2	Read single/multiple input status

Returns on/off status of any number of inputs (I). The maximum number of

inputs may be specified by the user (see below).

3	Read single/multiple holding registers

Returns contents of V memory. Holding registers are considered to be word

values under Modbus and that concept is used here. This area starts at V0. The

size (in words) can be specified by the user (see below).

4	Read single/multiple input registers

Read analog inputs. This function actually just returns the contents of a V

memory area separate from the holding registers. The user must add program

commands to read AI words and move them to V memory if desired. The V memory

area used by this command can be specified by the user (see below).

5	Force single coil (output)

Write to the output (Q) image register. The output is not really forced, just written.

6	Write singe holding register

Write a word to V memory.

15	Force multiple coils (outputs)

Write to multiple outputs (Qs). The starting output must begin on a byte boundary

(i.e. Q0.0 or Q2.0) and number of outputs written must be a multiple of eight. This

is not required under Modbus but was done here to simplify the implementation.

The output is not really forced, just written to the output image register.

16	Write multiple holding registers

Write multiple words to V memory. Up to 60 words can be written in one request.

The following memory locations are utilized to configure the Modbus driver. These locations are initialized in SBR 50 and may be modified by the user to change the size of the memory areas available via the Modbus driver to a host computer.

VW3290		Maximum number of inputs/outputs accessible via Modbus. This affects the

range of functions 1, 2, 5 and 15. The default is 64 (I0.0 to I7.7 and Q0.0

to Q7.7).

VW3294		Maximum number of input registers accessible via Modbus function 4. The

default is 16.

VW3296		Address in V memory where AI are to be read when responding to Modbus

function 4. The default value is VB2000.

VB4095 		Modbus address of the slave. The default value is address 1.

The following V memory locations are used by the Modbus driver and are not to be modified by the user.

M31.7				Flag used to signal a Modbus request has been received.

VB3300 - VB3559	Comm buffer

VB3560 - VB3575	Misc. scratch memory for Modbus

VB3580 - VB4091	CRC data table

Subroutines 50 - 63 are reserved for the Modbus driver.

Interrupts 120 - 127 are reserved for the Modbus driver.

Labels 254 and 255 are reserved for the Modbus driver.

The program size is 606 words.

| LAD (S7-MicroDOS) | STL (IEC) |
| --- | --- |
|  | Main Program |

// Call a subroutine to initialize the Modbus comm if this is the first scan.

// This rung should be placed somewhere near the top of the ladder program.

³ SM0.1                                                         50

1   ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³

LD	SM0.1	// If this is the first scan,

CALL	50	// initialize the Modbus comm

// Check to see if a Modbus request has been received. If one has, the receive

// interrupt routine sets M31.7.

// This rung should be somewhere near the end of the ladder program.

³

³ M31.7                                                         51

2   ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³          M31.7     K1

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(   R   )

³

³

3   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( MEND  )

³

LD	M31.7	// If Modbus request present,

CALL	51	// call the handler &

R	M31.7, 1	// clear request flag

MEND

Subroutines

// Subroutine 50

//

// Initialize the Modbus driver on port 0.

// NOTE: 	This initialization routine will require approximately 690 mSecs to execute due to the

//	initialization of the CRC table.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 50  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      MOV_WÄÄÄ¿

5   ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         K65´IN  OUTÃVW3290

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³       K1001´IN  OUTÃVW3292

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         K17´IN  OUTÃVW3294

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_DWÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³     &VB2000´IN  OUTÃVD3296

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K8´IN  OUTÃVW3574

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

// Initialize the memory limits for the various data type.

//

// NOTE: 	The maximum values stored should be one greater than the actual limit.

//	Example: To allow 32 outputs, use a value of 33.

SBR	50

LD	SM0.0

MOVW	65, VW3290	// max_IR = 64 bits

MOVW	1001, VW3292	// max. V words = 2000 bytes (1000 words)

MOVW	17, VW3294	// max. AI words = 16 words

MOVD	&VB2000, VD3296	// start of AI words in V memory

MOVW	8, VW3574	// load a constant value = 8 to be used in

// mathmatical operations

³                                               ³            MOV_BÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K1´IN  OUTÃVB4095

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

// Initialize the Modbus address.

MOVB	1, VB4095	// Modbus address = 1

³                                               ³            MOV_BÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        KH49´IN  OUTÃSMB30

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³               62

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³          M31.7     K1

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ(   R   )

// Initialize the port. See the S7-200 System Manual for other port configurations (i.e. baud rate, parity).

// RTU Modbus requires the use of eight data bits. The baud rate and parity may be changed.

//

// NOTE:	Setting the baud rate to 38.4K Baud will not function correctly.

MOVB	16#49, SMB30	// 9600 baud, 8 bits, even parity

// Initialize the CRC data table and reset the message pending flag.

CALL	62	// initialize the Modbus CRC table

R	M31.7, 1	// show no messages pending

³                                               ³

³                                               ³

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ(  ENI  )

³                                               ³

³                                               ³            MOV_BÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K6´IN  OUTÃSMB34

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K120´INT    ³

³                                               ³         K10´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                        K121´INT    ³

³                                                          K8´EVT    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

6   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

// The Modbus messages are delineated by a quiet line for at least 3.5 byte times which at 9600 baud

// is 4 milliseconds. The quiet line time is set to 6 mSecs to guarantee at least 5 mSecs (4 mSecs quiet

// line time + 1 mSec to receive a character).

//

// NOTE: This timeout must be changed for different baud rates. The times are:

//

//	300 baud	166  mSec

//	600	84

//	1200	43

//	2400	22

//	4800	12

//	9600	6

//	19.2K	5

ENI		// enable interrupts

MOVB	6, SMB34	// set quiet line timer for > 5 msec

ATCH	120, 10	// start search for quiet line

ATCH	121, 8	// INT 121 if we get a character

RET		// return

// Subroutine 51

//

// This subroutine processes the Modbus requests during the regular ladder scan.

//

// Calculate the CRC on the received message. When the CRC in the received message is included in

// the calculation, the result should always be a zero if there were no errors.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 51  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      MOV_WÄÄÄ¿

8   ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3300´IN  OUTÃAC0

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_DWÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³     &VB3302´IN  OUTÃAC1

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³               63

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³

³    K0          AC2                                            255

9   ÃÄÄÄÄÄÄÄ´ == W ÃÄÄÄÄÄÄÄÄÄÄ´NOTÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  JMP  )

³

SBR	51

LD	SM0.0

MOVW	VW3300, AC0	// get buffer length

MOVD	&VB3302, AC1	// get buffer address for CRC check

CALL	63	// calculate CRC

LDW=	0, AC2	// If (calculated CRC != 0),

NOT

JMP	255	// load an error

// The message looks good, so decide which Modbus function is being requested.

// The jump instruction following the call will always execute after the call returns

// since the subroutines will always set TOS to a 1 before returning.

³ SM0.0                                                      MOV_BÄÄÄ¿

10  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VB3303´IN  OUTÃAC0

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³    K1          AC0                                            52

11  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³               254

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(  JMP  )

³

³    K2          AC0                                            52

12  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³               254

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(  JMP  )

³

³    K3          AC0                                            53

13  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³               254

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(  JMP  )

³

³

³    K4          AC0                                            53

14  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³               254

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(  JMP  )

³

³    K5          AC0                                            54

15  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³               254

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(  JMP  )

³

³    K6          AC0                                            55

16  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³               254

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(  JMP  )

³

³    K15         AC0                                            56

17  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³               254

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(  JMP  )

³

³    K16         AC0                                            57

18  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³               254

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(  JMP  )

³

³ SM0.0                                                      MOV_WÄÄÄ¿

19  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K3´IN  OUTÃVW3300

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            WOR_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        KH80´IN1 OUTÃVW3302

³                                               ³      VW3302´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_BÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                          K1´IN  OUTÃVB3304

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

LD	SM0.0

MOVB	VB3303, AC0	// get the function from the request buffer

LDB=	1, AC0	// is this function 1?

CALL	52	// ...yes so service it

JMP	254	//  ...then jump to the end

LDB=	2, AC0	// is this function 2?

CALL	52	// ...yes so service it

JMP	254	//  ...then jump to the end

LDB=	3, AC0	// is this function 3?

CALL	53	// ...yes so service it

JMP	254	//  ...then jump to the end

LDB=	4, AC0	// is this function 4?

CALL	53	// ...yes so service it

JMP	254	//  ...then jump to the end

LDB=	5, AC0	// is this function 5?

CALL	54	// ...yes so service it

JMP	254	//  ...then jump to the end

LDB=	6, AC0	// is this function 6?

CALL	55	// ...yes so service it

JMP	254	//  ...then jump to the end

LDB=	15, AC0	// is this function 15?

CALL	56	// ...yes so service it

JMP	254	//  ...then jump to the end

LDB=	16, AC0	// is this function 16?

CALL	57	// ...yes so service it

JMP	254	//  ...then jump to the end

LD	SM0.0	// if none of the above...

MOVW	3, VW3300	//    load length for error response

ORW	16#0080, VW3302	//    set the MSBit of function to show error

MOVB	1, VB3304	//    load "function not supported" code

// The function has been serviced so calculate the CRC on the response and

// start the transmit of the response. Like the request, the length of the response

// will be in the first word of the buffer. This length will not include the CRC length

// and must be incremented by two before calling the transmit box.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ LBL:254  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      MOV_WÄÄÄ¿

21  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3300´IN  OUTÃAC0

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_DWÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³     &VB3302´IN  OUTÃAC1

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³               63

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³            MOV_DWÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³     &VB3302´IN  OUTÃAC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3300´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC2´IN  OUTÃ*AC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K2´IN1 OUTÃVW3300

³                                               ³      VW3300´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            XMTÄÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VB3301´TBL    ³

³                                               ³           0´POR    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K125´INT    ³

³                                               ³          K9´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

LBL	254

LD	SM0.0

MOVW	VW3300, AC0	// get the length

MOVD	&VB3302, AC1	// get buffer address for CRC check

CALL	63	// calculate CRC

MOVD	&VB3302, AC3	// get address of buffer start

+I	VW3300, AC3	// point to end of buffer

MOVW	AC2, *AC3	// put the CRC in buffer

+I	2, VW3300	// add two bytes for CRC

XMT	VB3301, 0	// transmit the response

ATCH	125, 9	// goto INT 125 when xmit complete

CRET

// Error handler for CRC or length problems.

//

// There is not really much to be done in the cases where the CRC indicates an

// error or if not enough bytes were received to process a message, except

// to just reset the comm to look for the next message and let the master time

// out on this one.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ LBL:255  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      ATCHÄÄÄÄ¿

23  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K120´INT    ³

³                                               ³         K10´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                        K121´INT    ³

³                                                          K8´EVT    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

24  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

LBL	255

LD	SM0.0

ATCH	120, 10	// start search for quiet line

ATCH	121, 8	// INT 121 if we get a character

RET

// Subroutine 52

//

// This subroutine supports Modbus functions 1 and 2 by reading the status of one or

// more outputs or inputs. The bits in the response are packed eight bits per byte.

// The first requested output/input will be in the LSBit of the first data byte. If the

// number of requested outputs/inputs is not divisible by eight, the MSBits of the

// last data byte are to be filled with zeros, but this is not currently done.

//

// The format for the request is:

//    addr    01    start_bit (MSB,LSB)    bit_count (MSB,LSB)

//

// The start_bit is the first output/input requested (zero based).

// The bit_count is the number of outputs/inputs requested.

//

// The format for the response is:

//    addr    01    byte_count    data.....

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 52  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      ADD_IÄÄÄ¿

26  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VW3304´IN1 OUTÃAC0

³                                                      VW3306´IN2    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³ SM1.1                                                         61

27  ÃÄ´   ÃÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³       ³               ³                       ³

³V3304.7³               ³                       ³

ÃÄ´   ÃÄ´               ³                       ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

³       ³               ³

³V3306.7³               ³

ÃÄ´   ÃÄÙ               ³

³                       ³

³    AC0       VW3290   ³

ÃÄÄÄÄÄÄÄ´ >= W ÃÄÄÄÄÄÄÄÄÙ

// Check to see if the max. number of outputs or inputs has been exceeded.

SBR	52

LD	SM0.0

MOVW	VW3304, AC0	// get the start_bit value

+I	VW3306, AC0	// ...plus the bit_count

LD	SM1.1	// if (overflow) or

O	V3304.7	//    (start_bit < 0) or

O	V3306.7	//    (bit_count < 0) or

OW>=	AC0,VW3290	//    (last_bit_ number > max_IR)

CALL	61	//    build error response

CRET		//    return

// Determine which area we are working with and then copy either the inputs or

// outputs to a scratch area within the comm buffer (but not used in this response),

// and set the following byte to zero.  This allows the method of shifting

// used in the next section to work properly.

//

// NOTE: 	This is set up for an image register size of 8 bytes. If the image

//	register size changes to greater than 8 bytes, the constant on the

// 	block move instruction must be changed.

//

// Get the start_bit number and determine the address of the first byte to copy.

// After the divide, the value in VW3560 is the remainder (shift count) and

// the value in VW3562 is the quotient (byte offset into outputs or inputs).

³    K1        VB3303                                        MOV_DWÄÄ¿

28  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                       ³                                    ³       ³

³                       ³                                &QB0´IN  OUTÃAC3

³                       ³                                    ³       ³

³                       ³                                    ÀÄÄÄÄÄÄÄÙ

³                       ³                                    MOV_DWÄÄ¿

³                       ÀÄ´NOTÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                        &IB0´IN  OUTÃAC3

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³ SM0.0                                                      BLKMOV_B¿

29  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        *AC3´IN  OUTÃVB3340

³                                               ³          K8´N      ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_BÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K0´IN  OUTÃVB3348

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_DWÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³     &VB3340´IN  OUTÃAC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            DIVÄÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3304´IN1 OUTÃVD3560

³                                               ³      VW3574´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3562´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3306´IN1 OUTÃAC1

³                                               ³          K7´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            SHR_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC1´IN  OUTÃAC1

³                                               ³          K3´N      ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC1´IN1 OUTÃVW3300

³                                               ³          K3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_BÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                         AC1´IN  OUTÃVB3304

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

LDB=	1,VB3303	// if function 1 (outputs)

MOVD	&QB0, AC3	//    then point to outputs

NOT		// else

MOVD	&IB0, AC3	//    point to inputs

LD	SM0.0

BMB	*AC3, VB3340, 8	// copy inputs/outputs to scratch area

MOVB	0, VB3348	// zero out the "next" byte in scratch area

MOVD	&VB3340, AC3	// source pointer = addr of the scratch area

MOVW	VW3304, VW3562	// get the start_bit value

DIV	VW3574, VD3560	// start_bit / 8

+I	VW3562, AC3	// add offset to source pointer

// Get the bit_count and determine the number of bytes we need to send back in the response.

MOVW	VW3306, AC1	// get the bit_count

+I	7, AC1	// round it up

SRW	AC1, 3	// divide by 8 bits/byte

// Load the response buffer size and the byte_count into the response buffer.

MOVW	AC1, VW3300	// get the byte_count

+I	3, VW3300	// add three bytes for header

MOVB	AC1, VB3304	// load byte_count

// Get the data from the image register, shift it into position and place it in the response buffer.

//

// The method used is to fetch a word of image register with the byte we really want

// in the MSByte of the word.  The word is rotated for shift_count number of bits.

// This shifts the LSBits of the "next" IR byte into the MSBits of the byte we want.

// When the shift is complete, we get the byte into the LSByte of the word with a swap

// instruction and then move the byte into the response buffer.

³ SM0.0                                                      MOV_DWÄÄ¿

30  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³     &VB3305´IN  OUTÃAC2

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            FORÄÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3562´IDX    ³

³                                               ³            ³       ³

³                                               ³          K1´ITL    ³

³                                               ³            ³       ³

³                                               ³         AC1´FNL    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ROR_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        *AC3´IN  OUTÃAC0

³                                               ³      VB3561´N      ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            SWAPÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC0´IN     ³

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_BÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC0´IN  OUTÃ*AC2

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            INC_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC2´IN  OUTÃAC2

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            INC_WÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                         AC3´IN  OUTÃAC3

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

31  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( NEXT  )

³

³

32  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

LD	SM0.0

MOVD	&VB3305, AC2	// load pointer to response buffer

FOR	VW3562, 1, AC1	// for byte_count bytes

MOVW	*AC3,AC0	//    get a word of outputs

RRW	AC0, VB3561	//    shift it right

SWAP	AC0	//    move the byte to the LSByte

MOVB	AC0, *AC2	//    store the byte

INCW	AC2	//    increment buffer pointer

INCW	AC3	//    increment image register pointer

NEXT		// end for

RET

// Subroutine 53

//

// This subroutine supports Modbus function 3 (read output/holding registers)

// and function 4 (read input registers). The output/holding registers are

// considered to be V memory in this PLC. The input registers are considered

// to be analog inputs.

//

// NOTE: 	The analog inputs are not directly read by this routine since the PLC

//	will not allow indirect access to the analog values. The analog inputs

//	are read starting from the V memory location specified in VD3296. This

//	location should be set up in the initialization subroutine. It is the user's

//	responsibility to move the analog data into the V memory.

//

// The format for the request is:

//

//     addr    03    start_word (MSB,LSB)    word_count (MSB,LSB)

//

// The start_word is the first word requested (zero based).

// The word_count is the number of words requested.

//

// The format for the response is:

//

//    addr    03    byte_count    data

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 53  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      ADD_IÄÄÄ¿

34  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VW3304´IN1 OUTÃAC0

³                                                      VW3306´IN2    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³ SM1.1                                                         61

35  ÃÄ´   ÃÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³       ³               ³                       ³

³V3304.7³               ³                       ³

ÃÄ´   ÃÄÙ               ³                       ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

³                       ³

³  VW3306       K126    ³

ÃÄÄÄÄÄÄÄ´ >= W ÃÄÄÄÄÄÄÄÄ´

³                       ³

³V3306.7                ³

ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

³

³    K3        VB3303                                        MOV_WÄÄÄ¿

36  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                       ³                       ³            ³       ³

³                       ³                       ³      VW3292´IN  OUTÃAC1

³                       ³                       ³            ³       ³

³                       ³                       ³            ÀÄÄÄÄÄÄÄÙ

³                       ³                       ³            MOV_DWÄÄ¿

³                       ³                       ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                       ³                                    ³       ³

³                       ³                                &VB0´IN  OUTÃAC2

³                       ³                                    ³       ³

³                       ³                                    ÀÄÄÄÄÄÄÄÙ

³                       ³                                    MOV_WÄÄÄ¿

³                       ÀÄ´NOTÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3294´IN  OUTÃAC1

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_DWÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VD3296´IN  OUTÃAC2

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³    AC0         AC1                                            61

37  ÃÄÄÄÄÄÄÄ´ >= W ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

// Check to see if the max. memory limit has been exceeded.

SBR	53

LD	SM0.0

MOVW	VW3304, AC0	// get the start_word value

+I	VW3306, AC0	// ...plus the word_count

LD	SM1.1	// if (overflow) or

O	V3304.7	//    (start_word < 0) or

OW>= 	VW3306, 126	//    (word_count > 125) or

O	V3306.7	//    (word_count < 0)

CALL	61	//    build error response

CRET		//    return

LDB=	3,VB3303	// if function 3 (V memory)

MOVW	VW3292, AC1	//    get max. V memory size

MOVD	&VB0, AC2	//    source_pointer = V memory

NOT		// else

MOVW	VW3294, AC1	//    get max. AI word size

MOVD	VD3296, AC2	//    source_pointer = AI memory

LDW>=   AC0, AC1	// if start_word + word_count >= memory size

CALL	61	//    build error response

CRET		//    return

// The request is OK so get the start_word, double it for a byte offset and add it to the source_pointer.

// Point the response buffer and move the  data there.

³

³ SM0.0                                                      ADD_IÄÄÄ¿

38  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3304´IN1 OUTÃAC2

³                                               ³         AC2´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3304´IN1 OUTÃAC2

³                                               ³         AC2´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3306´IN1 OUTÃAC1

³                                               ³      VW3306´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_BÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC1´IN  OUTÃVB3304

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K3´IN1 OUTÃAC1

³                                               ³         AC1´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC1´IN  OUTÃVW3300

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3306´IN  OUTÃAC1

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            BLKMOV_W¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                        *AC2´IN  OUTÃVW3305

³                                                         AC1´N      ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

39  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

LD	SM0.0

+I	VW3304, AC2	// add start_word to source_pointer

+I	VW3304, AC2	//   ...start_word * 2 to source_pointer

MOVW	VW3306, AC1	// get the word count

+I	VW3306, AC1	// ...times two for a byte count

MOVB	AC1, VB3304	//   ...store byte count of response

+I	3, AC1	// add overhead bytes

MOVW	AC1,VW3300	//   ...store response buffer size

MOVW	VW3306, AC1	// get the word count again

BMW	*AC2, VW3305, AC1	// copy data from source to buffer

RET		// return

// Subroutine 54

//

// This subroutine supports Modbus function 5 to force a single output either on or off.

//

// The format for the request is:

//

//    addr    05    output_bit (MSB,LSB)    data (FF00 or 0000)

//

// The data value FF00 turns on the output, the value 0000 turns off the output. Any other data values

// result in no action being taken.

//

// The response message is to retransmit the request message.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 54  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      INC_WÄÄÄ¿

41  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VW3304´IN  OUTÃAC0

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³    AC0       VW3290                                           61

42  ÃÄÄÄÄÄÄÄ´ >= W ÃÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                       ³                       ³

³V3304.7                ³                       ³

ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                       ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

³

³  VW3306        K0                                          MOV_WÄÄÄ¿

43  ÃÄÄÄÄÄÄÄ´ == W ÃÄÄÄÄÄÄÄÄÂÄ´NOTÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                       ³                       ³            ³       ³

³  VW3306      KHFF00   ³                       ³          K6´IN  OUTÃVW3300

ÃÄÄÄÄÄÄÄ´ == W ÃÄÄÄÄÄÄÄÄÙ                       ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

SBR	54

LD	SM0.0

MOVW	VW3304, AC0	// get output_bit

INCW	AC0	// ...and fix it for check

LDW>=	AC0, VW3290	// if (output_bit > max_IR_number) or

O	V3304.7	//    (output_bit < 0)

CALL	61	//    build error response

CRET // return

// Check to see if the data is either FF00 or 0000. If the data is not one of these values then no action

// is taken except to echo the request back to the master.

LDW=	VW3306, 0	// if (data != 0) or

OW=	VW3306, 16#FF00	//    (data != FF00)

NOT

MOVW	6, VW3300	//    set response length

CRET		//    return

// Determine which byte of the outputs and which bit of the byte to modify.

// This is done by dividing the output bit by eight. The quotient is the byte offset, and the remainder

// is the bit number.

//

// After the divide, the value in VW3560 is the remainder (bit number), and

// the value in VW3562 is the quotient (offset into outputs).

³

³ SM0.0                                                      DIVÄÄÄÄÄ¿

44  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3304´IN1 OUTÃVD3560

³                                               ³      VW3574´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_DWÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        &QB0´IN  OUTÃAC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3562´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_BÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        *AC3´IN  OUTÃAC2

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            SHL_WÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                          K1´IN  OUTÃAC1

³                                                      VB3561´N      ³

³                                                            ÀÄÄÄÄÄÄÄÙ

LD	SM0.0

MOVW	VW3304, VW3562	// get the output_bit

DIV	VW3574, VD3560	// output_bit / 8

MOVD	&QB0, AC3	// point to outputs

+I	VW3562, AC3	// offset point to correct byte

MOVB	*AC3, AC2	// get the output byte

MOVW	1, AC1	// create a mask

SLW	AC1, VB3561	// ...for the proper bit

³  VB3306        K0                                          INV_WÄÄÄ¿

45  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                       ³                       ³            ³       ³

³                       ³                       ³         AC1´IN  OUTÃAC1

³                       ³                       ³            ³       ³

³                       ³                       ³            ÀÄÄÄÄÄÄÄÙ

³                       ³                       ³            WAND_WÄÄ¿

³                       ³                       ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                       ³                                    ³       ³

³                       ³                                 AC1´IN1 OUTÃAC2

³                       ³                                 AC2´IN2    ³

³                       ³                                    ÀÄÄÄÄÄÄÄÙ

³                       ³                                    WOR_WÄÄÄ¿

³                       ÀÄ´NOTÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                         AC1´IN1 OUTÃAC2

³                                                         AC2´IN2    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

LDB=	VB3306, 0	// if data == 0

INVW	AC1	//    make a clearing mask

ANDW	AC1, AC2	//    clear the bit

NOT		// else

ORW	AC1, AC2	//    set the bit

³ SM0.0                                                      MOV_BÄÄÄ¿

46  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC2´IN  OUTÃ*AC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                          K6´IN  OUTÃVW3300

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

47  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

LD	SM0.0

MOVB	AC2, *AC3	// restore the output byte

MOVW	6, VW3300	// set response length

RET

// Subroutine 55

//

// This subroutine supports Modbus function 6 by writing to a single holding register in the PLC.

// The holding registers are considered to be V memory in this implementation.

//

// The format for the request is:

//

//    addr    06    start_word (MSB,LSB)    data (MSB,LSB)

//

// The start_word is the first word requested (zero based).

// The data is the word to be written to the PLC.

//

// The format for the response is the same as the request:

//

//    addr    06    start_word (MSB,LSB)    data (MSB,LSB)

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 55  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      DEC_WÄÄÄ¿

49  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VW3292´IN  OUTÃAC0

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³  VW3304        AC0                                            61

50  ÃÄÄÄÄÄÄÄ´ >= W ÃÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                       ³                       ³

³V3304.7                ³                       ³

ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                       ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

³

// Check to see if the max. memory limit has been exceeded.

SBR	55

LD	SM0.0

MOVW	VW3292, AC0	// get memory size + 1 value

DECW	AC0	// ...and make it just memory size

LDW>=	VW3304, AC0	// if (start_word >= memory size) or

O	V3304.7	//    (start_word < 0)

CALL	61	//    build error response

CRET		//    return

// The request is OK so get the start_word, double it for a byte offset, and

// add it to the source_pointer. Move the data from the request to V memory.

³ SM0.0                                                      MOV_DWÄÄ¿

51  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        &VB0´IN  OUTÃAC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3304´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3304´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3306´IN  OUTÃ*AC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                          K6´IN  OUTÃVW3300

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

52  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

LD	SM0.0

MOVD	&VB0, AC3	// source_pointer = V memory

+I	VW3304, AC3	// add in the offset...

+I	VW3304, AC3	// ...twice for a byte offset

MOVW	VW3306, *AC3	// store data to V memory

MOVW	6, VW3300	// set response length

RET		// return

// Subroutine 56

//

// This subroutine supports Modbus function 15 (forcing multiple coils). The outputs are packed

// eight bits to a byte. The LSBit of the first byte of data is written to the start_bit location.

// Subsequent bits are written to consecutive locations.

//

// NOTE:	This implementation will return an error if the start_bit and the 	bit_count values are not

//	multiples of eight. It is just too complicated in STL or LAD to handle starting on any bit.

//

// The format for the request is:

//

//   addr    0F    start_bit (MSB,LSB)    bit_count (MSB,LSB)    byte_count    data

//

// The start_bit is the first output to be written and is the LSBit of the first data byte.

// The bit_count is the number of outputs to be written.

// The byte_count is the number of data bytes.

//

// The format for the response is:

//

//    addr    0F    start_bit(MSB,LSB)    bit_count(MSB,LSB)

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 56  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      ADD_IÄÄÄ¿

54  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VW3304´IN1 OUTÃAC0

³                                                      VW3306´IN2    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³ SM1.1                                                         61

55  ÃÄ´   ÃÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³       ³               ³                       ³

³V3304.7³               ³                       ³

ÃÄ´   ÃÄ´               ³                       ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

³       ³               ³

³V3306.7³               ³

ÃÄ´   ÃÄÙ               ³

³                       ³

³    AC0       VW3290   ³

ÃÄÄÄÄÄÄÄ´ >= W ÃÄÄÄÄÄÄÄÄÙ

³

// Check to see if the max. number of outputs has been exceeded.

SBR	56

LD	SM0.0

MOVW	VW3304, AC0	// get the start_bit value

+I	VW3306, AC0	// ...plus the bit_count

LD	SM1.1	// if (overflow) or

O	V3304.7	//    (start_bit < 0) or

O	V3306.7	//    (bit_count < 0) or

OW>=	AC0, VW3290	//    (last_address > max_IR)

CALL	61	//    build error response

CRET		//    return

// Determine the byte and bit offset into the output IR, and the full and partial bytes to be written.

//

// After the divide, the value in VW3560 is the remainder (shift count), and

// the value in VW3562 is the quotient (byte offset into outputs).

//

// After the divide, the value in VW3564 is the remainder, and the value in

// VW3566 is the number of full bytes to be written.

³ SM0.0                                                      DIVÄÄÄÄÄ¿

56  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3304´IN1 OUTÃVD3560

³                                               ³      VW3574´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            DIVÄÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3306´IN1 OUTÃVD3564

³                                               ³      VW3574´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VW3566´IN1 OUTÃAC0

³                                                          K9´IN2    ³

³ ÀÄÄÄÄÄÄÄÙ

LD	SM0.0

MOVW	VW3304, VW3562	// get the start_bit value

DIV	VW3574, VD3560	// start_bit / 8

MOVW	VW3306, VW3566	// get the bit_count

DIV	VW3574, VD3564	// bit_count / 8

MOVW	VW3566, AC0	// get (bit_count / 8)

+I	9, AC0	// ...plus 9 bytes of overhead

// Make sure that the host sent enough data with the request.  The buffer length

// should be equal to the (bit_count / 8) + 9 bytes of overhead.

³  VB3301        AC0                                            61

57  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄ´NOTÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³                                               ³

³                                               ³

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

³

LDB=	VB3301, AC0	// if (calculated length ( received length)

NOT

CALL	61	//    show an error

CRET		//    return

// Determine if we are dealing with a "nice" frame where the start_bit is the first bit of a byte and

// the bit_count is a whole number of bytes. If this is not the case, return an error to the host.

³  VB3561        K0        VB3565        K0                  MOV_DWÄÄ¿

58  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        &QB0´IN  OUTÃAC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3562´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            BLKMOV_B¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VB3309´IN  OUTÃ*AC3

³                                               ³      VB3567´N      ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K6´IN  OUTÃVW3300

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

LDB=	VB3561, 0	// if (start_bit is bit zero of the byte) and

AB=	VB3565, 0	//    (whole bytes = TRUE)

MOVD	&QB0, AC3	//    point to outputs

+I	VW3562, AC3	//    add offset to starting output

BMB	VB3309, *AC3, VB3567	//    copy request data to outputs

MOVW	6, VW3300	//    set response length

CRET		//    return

// This was not a nice frame so take the easy way out and abort the request.

³ SM0.0                                                         61

59  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³

³

60  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

LD	SM0.0	// else

CALL	61	//    show an error

RET		//    return

// Subroutine 57

//

// This subroutine supports Modbus function 16 (writing up to 60 holding registers to the PLC).

// The holding registers are considered to be V memory in this implementation.

//

// NOTE:	The max. value of 60 registers (120 bytes) is a limitation noted in the Modbus specification.

//

// The format for the request is:

//    addr    10    start_word (MSB,LSB)    word_count (MSB,LSB)    byte_count   data…

//

// The format for the response is the same as the request:

//    addr    10    start_word (MSB,LSB)    word_count (MSB,LSB)

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 57  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      ADD_IÄÄÄ¿

62  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VW3304´IN1 OUTÃAC0

³                                                      VW3306´IN2    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³ SM1.1                                                         61

63  ÃÄ´   ÃÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ( CALL  )

³       ³               ³                       ³

³V3304.7³               ³                       ³

ÃÄ´   ÃÄ´               ³                       ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRET  )

³       ³               ³

³V3306.7³               ³

ÃÄ´   ÃÄÙ               ³

³                       ³

³    AC0       VW3292   ³

ÃÄÄÄÄÄÄÄ´ >= W ÃÄÄÄÄÄÄÄÄÙ

³

// Calculate the last word address requested by adding the word_count to the start_word.

// If this last address is greater than the max. V memory address available, then return an error.

SBR	57

LD	SM0.0

MOVW	VW3304, AC0	// get the start_word

+I	VW3306, AC0	// ...plus word_count

LD	SM1.1	// if (overflow) or

O	V3304.7	//    (start_word < 0) or

O	V3306.7	//    (word_count < 0) or

OW>=	AC0, VW3292	//    (last address >= memory size)

CALL	61	//    build error response

CRET		//    return

// Compare the number of bytes received to the word_count from the message

// to be sure that we received enough data bytes. The receive byte_count

// should equal the (word_count * 2) + 9 overhead bytes. Also verify that the

// word count is no greater than 60 (120 bytes), the max allowed by the function.

//

// Also verify that the word_count * 2 is equal to the byte_count.  It is a little

// redundant to double check all of these fields, but we should be complete.

³ SM0.0                                                      SHL_WÄÄÄ¿

64  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3306´IN  OUTÃAC0

³                                               ³          K1´N      ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            SUB_IÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VW3300´IN1 OUTÃVW3300

³                                                          K9´IN2    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³  VW3300        AC0         AC0       VB3308                   61

65  ÃÄÄÄÄÄÄÄ´ == W ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄ´NOTÃÄÄÄÂÄÄ( CALL  )

³                                                         ³

³    AC0        K121                                      ³

ÃÄÄÄÄÄÄÄ´ >= W ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄ( CRET  )

³

LD	SM0.0

MOVW	VW3306, AC0	// get the word_count

SLW	AC0, 1	// word_count * 2

-I	9, VW3300	// receive byte_count - 9

LDW=	VW3300, AC0	// if (word_count * 2 != receive count - 9) or

AB=	AC0, VB3308	//    (word_count * 2 != byte_count) or

NOT

OW>=	AC0, 121	//    (count > 60 words + overhead)

CALL	61	//    build error response

CRET		//    return

// The request is OK so get the start_word, double it for a byte offset and then

// add it to the source_pointer. Move the data from the request to V memory.

³ SM0.0                                                      MOV_DWÄÄ¿

66  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        &VB0´IN  OUTÃAC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3304´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3304´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            BLKMOV_W¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3309´IN  OUTÃ*AC3

³                                               ³      VB3307´N      ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                          K6´IN  OUTÃVW3300

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

67  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

LD	SM0.0

MOVD	&VB0, AC3	// source_pointer = V memory

+I	VW3304, AC3	// add in the offset...

+I	VW3304, AC3	// ...twice for a byte offset

BMW	VW3309, *AC3, VB3307	// store data to V memory

MOVW	6, VW3300	// set response length

RET		// return

// Subroutine 61

//

// This subroutine sets up the response buffer for Modbus exception code two.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 61  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      MOV_WÄÄÄ¿

69  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K3´IN  OUTÃVW3300

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            WOR_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        KH80´IN1 OUTÃVW3302

³                                               ³      VW3302´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_BÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                          K2´IN  OUTÃVB3304

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

70  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

SBR	61

LD	SM0.0

MOVW	3, VW3300	// load length for error response

ORW	16#0080, VW3302	// set the MSBit of function to show error

MOVB	2, VB3304	// load exception code

RET

// Subroutine 62

//

// This subroutine generates the CRC table used to calculate the CRC values in the message.

//

// The polynomial used is :  x16 + x15 + x2 + 1

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 62  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      MOV_DWÄÄ¿

72  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³     &VB3580´IN  OUTÃAC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_DWÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K0´IN  OUTÃAC2

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            FORÄÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3560´IDX    ³

³                                               ³            ³       ³

³                                               ³          K1´ITL    ³

³                                               ³            ³       ³

³                                               ³        K256´FNL    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC2´IN  OUTÃAC0

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            FORÄÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3562´IDX    ³

³                                               ³            ³       ³

³                                               ³          K1´ITL    ³

³                                               ³            ³       ³

³                                               ³          K8´FNL    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            SHR_WÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                         AC0´IN  OUTÃAC0

³                                                          K1´N      ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³ SM1.1                                                      WXOR_WÄÄ¿

73  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      KHA001´IN1 OUTÃAC0

³                                                         AC0´IN2    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

74  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( NEXT  )

³

³ SM0.0                                                      INC_WÄÄÄ¿

75  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC2´IN  OUTÃAC2

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC0´IN  OUTÃ*AC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K2´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(  WDR  )

³

³

76  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( NEXT  )

³

³

77  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

SBR	62

LD	SM0.0

MOVD	&VB3580, AC3	// load table_pointer

MOVD	0, AC2	// load index

FOR	VW3560, 1, 256	// for all possible byte values

MOVW	AC2, AC0	//    value = index

FOR	VW3562, 1, 8	//    for eight bits per byte

SRW	AC0, 1	//        shift out the LSBit

LD	SM1.1	//        if bit shifted out is a one

XORW	16#A001, AC0	//        XOR crc with value

NEXT		//        end for

LD	SM0.0

INCW	AC2	//    increment index

MOVW	AC0, *AC3	//    store table word

+I	2, AC3	//    increment table pointer

WDR		//    reset the watchdog

NEXT		// end for

RET

// Subroutine 63

//

// This subroutine calculates the CRC value for the message using the faster

// table lookup method.

//

// Inputs :	AC0      message length

// 	AC1      pointer to message

//

// Outputs: 	AC2    CRC value in LSWord

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ SBR: 63  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0

79  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ(  WDR  )

³                                               ³

³                                               ³            MOV_DWÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³   KH8000000´IN  OUTÃAC3

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_DWÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      KHFFFF´IN  OUTÃAC2

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            FORÄÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3560´IDX    ³

³                                               ³            ³       ³

³                                               ³          K1´ITL    ³

³                                               ³            ³       ³

³                                               ³         AC0´FNL    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_BÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        *AC1´IN  OUTÃAC3

³                                               ³            ³       ³

³ ³ ÀÄÄÄÄÄÄÄÙ

³                                               ³            WXOR_WÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC2´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            WAND_WÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        KHFF´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            SHL_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC3´IN  OUTÃAC3

³                                               ³          K1´N      ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ADD_IÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³       K3580´IN1 OUTÃAC3

³                                               ³         AC3´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            SWAPÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC2´IN     ³

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            WAND_WÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        KHFF´IN1 OUTÃAC2

³                                               ³         AC2´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            WXOR_WÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        *AC3´IN1 OUTÃAC2

³                                               ³         AC2´IN2    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            INC_WÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                         AC1´IN  OUTÃAC1

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

80  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( NEXT  )

³

³                                                            SWAPÄÄÄÄ¿

81  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³         AC2´IN     ³

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(  WDR  )

³

³

82  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ(  RET  )

³

SBR	63

LD	SM0.0

WDR		// reset the watchdog timer

MOVD	16#08000000, AC3	// clear temporary register

MOVD	16#0000FFFF, AC2	// initialize the CRC value to 0xFFFF

FOR	VW3560, 1, AC0	// for all bytes in the message

MOVB	*AC1, AC3	//    get the message byte

XORW	AC2, AC3	//    XOR data with CRC

ANDW	16#00FF, AC3	//    keep only the LSByte

SLW	AC3, 1	//    convert to an index into word table

+I	3580, AC3	//    add start of table address (VB3580)

SWAP	AC2	//    swap bytes of CRC

ANDW	16#00FF, AC2	//    keep only the LSByte

XORW	*AC3, AC2	//    OR table value with CRC

INCW	AC1	//    point to the next message byte

NEXT		// end for

SWAP	AC2	// swap bytes in CRC before returning

WDR		// reset the watchdog timer

RET

Interrupt routines

// INT 120

//

// This interrupt routine will execute if the quiet line timer expires. When this happens, attach the main

// character receive interrupt to the port since the next character we receive should be the start of a

// message.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ INT:120  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      DTCHÄÄÄÄ¿

84  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          10´EVT    ³

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K122´INT    ³

³                                               ³          K8´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          K0´IN  OUTÃVW3300

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_DWÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                     &VB3302´IN  OUTÃVD3570

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

85  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( RETI  )

³

INT	120

LD	SM0.0

DTCH	10	// disable quiet line timer

ATCH	122, 8	// attach receive routine to comm port

MOVW	0, VW3300	// set receive count to zero

MOVD	&VB3302, VD3570	// set pointer to receive buffer

RETI

// INT 121

//

// This interrupt routine handles the serial port interrupts while looking for a quiet

// line. If there is a character received during the quiet line search the action is to

// restart the quiet line timer.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ INT:121  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      ATCHÄÄÄÄ¿

87  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                        K120´INT    ³

³                                                         K10´EVT    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

88  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( RETI  )

³

INT	121

LD	SM0.0

ATCH	120,10	// re-enable the quiet line timer

RETI

// INT 122

//

// This routine will receive the first byte of the message after finding the

// quiet line time. The first byte of the message will be the address.  Check

// to see if this is a request to this address. If it is, attach INT 123 to receive the entire message.

// If the message is not for this address then go back to looking for a quiet line time.

//

// NOTE:	The broadcast address is not supported in this implementation as

//	it would add extra code. If this feature is desired, this INT would

//	have to be modified along with all of the function handlers, since

//	the broadcast address is not supported by all functions.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ INT:122  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM3.0                                                      ATCHÄÄÄÄ¿

90  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K120´INT    ³

³                                               ³         K10´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K121´INT    ³

³                                               ³          K8´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRETI )

³

INT	122

LD	SM3.0	// if (parity error)

ATCH	120, 10	//    start search for quiet line

ATCH	121, 8	//    INT 1 if we get a character

CRETI		//    return

³   SMW2       VB4095                                        MOV_BÄÄÄ¿

91  ÃÄÄÄÄÄÄÄ´ == B ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        SMB2´IN OUT *VD3570

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            INC_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3572´IN  OUTÃVW3572

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            INC_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3300´IN  OUTÃVW3300

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K123´INT    ³

³                                               ³          K8´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K124´INT    ³

³                                               ³         K10´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ( CRETI )

// else (parity is OK)

LDB=	SMB2, VB4095	//    if (address = my address)

MOVB	SMB2, *VD3570	//        store address in buffer

INCW	VW3572	//        increment buffer pointer

INCW	VW3300	//        increment receive byte counter

ATCH	123, 8	//        receive rest of message

ATCH	124, 10	//        end receive if timeout

CRETI		//        return

³ SM0.0                                                      ATCHÄÄÄÄ¿

92  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K120´INT    ³

³                                               ³         K10´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                        K121´INT    ³

³                                                          K8´EVT    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

93  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( RETI  )

³

LD	SM0.0	//    else (address != my address)

ATCH	120,10	//        re-enable the quiet line timer

ATCH	121,8	//        INT 121 if we get a character

RETI

// INT 123

//

// This is the main character interrupt service routine. Characters are received, checked for

// parity errors and then placed in the comm buffer. The byte count is incremented for each character.

// If the number of bytes received is greater than 256 then the receive is aborted.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ INT:123  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      ATCHÄÄÄÄ¿

95  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K124´INT    ³

³                                               ³         K10´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            MOV_BÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        SMB2´IN OUT *VD3570

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            INC_WÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³      VW3572´IN  OUTÃVW3572

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            INC_WÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                      VW3300´IN  OUTÃVW3300

³                                                            ³       ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³ SM3.0                                                      ATCHÄÄÄÄ¿

96  ÃÄ´   ÃÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³       ³                                       ³            ³       ³

³V3300.0³                                       ³        K120´INT    ³

ÃÄ´   ÃÄÙ                                       ³         K10´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                        K121´INT    ³

³                                                          K8´EVT    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

97  ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( RETI  )

³

INT	123

LD	SM0.0

ATCH	124, 10	// message complete on next timeout

MOVB	SMB2, *VD3570	// store message byte in buffer

INCW	VW3572	// increment buffer pointer

INCW	VW3300	// increment receive byte counter

LD	SM3.0	// if (parity error) or

O	V3300.0	//    (buffer overflow)

ATCH	120, 10	//    start search for quiet line

ATCH	121, 8	//    INT 1 if we get a character

RETI

// INT 124

//

// This interrupt routine will execute when a message has been received and we have found another

// quiet line meaning that the request is compete. The action here is to disable the quiet line timer,

// disable the port interrupt, and set a flag for the background scan to process the message.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ INT:124  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      DTCHÄÄÄÄ¿

99  ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³          10´EVT    ³

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            DTCHÄÄÄÄ¿

³                                               ÃÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³           8´EVT    ³

³                                               ³            ³       ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³          M31.7     K1

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ(   S   )

³

³

100 ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( RETI  )

³

INT	124

LD	SM0.0

DTCH	10	// disable quiet line timer

DTCH	8	// disable port interrupt

S	M31.7, 1	// flag background

RETI

// INT 125

//

// This interrupt routine will execute when the response has been completely transmitted back to

// the master. Reset the interrupt system to again search for a quiet line and the start of a new request.

ÚÄÄÄÄÄÄÄÄÄÄ¿

³ INT:125  ³

ÀÄÄÄÂÄÄÄÄÄÄÙ

³ SM0.0                                                      ATCHÄÄÄÄ¿

102 ÃÄ´   ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                               ³            ³       ³

³                                               ³        K120´INT    ³

³                                               ³         K10´EVT    ³

³                                               ³            ÀÄÄÄÄÄÄÄÙ

³                                               ³            ATCHÄÄÄÄ¿

³                                               ÀÄÄÄÄÄÄÄÄÄÄÄÄ´EN     ³

³                                                            ³       ³

³                                                        K121´INT    ³

³                                                          K8´EVT    ³

³                                                            ÀÄÄÄÄÄÄÄÙ

³

103 ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ( RETI  )

³

INT	125

LD	SM0.0

ATCH	120,10	// start search for quiet line

ATCH	121,8	// INT 1 if we get a character

RETI

Conversion Notes

To Convert from IEC STL to S7-Micro/DOS STL:

(  Add a ‘K’ before all non-Hex numerical constants (i.e. 4 ( K4)

(  Replace ‘16#’ with ‘KH’ for all Hex constants (i.e. 16#FF ( KHFF)

(  Commas denote field divisions.  Use arrow or TAB keys to toggle between fields.

(  To convert an S7-Micro/DOS STL program to LAD form, every network must begin with the word ‘NETWORK’ and a number.  Each network in this Application Tip program is designated by a number on the ladder diagram.  Use the INSNW command under the EDIT menu to enter a new network.  The MEND, RET, RETI, LBL, SBR, and INT commands each receive their own networks.

(   Line-Comments denoted by ‘//’ are not possible with S7-Micro/DOS, but Network-Comments are possible.

General Notes

The SIMATIC S7-200 Application Tips are provided to give users of the S7-200 some indication as to how, from the view of programming technique, certain tasks can be solved with this controller. These instructions do not purport to cover all details or variations in equipment, nor do they provide for every possible contingency. Use of the S7-200 Application Tips is free.

Siemens reserves the right to make changes in specifications shown herein or make improvements at any time without notice or obligation. It does not relieve the user of responsibility to use sound practices in application, installation, operation, and maintenance of the equipment purchased. Should a conflict arise between the general information contained in this publication, the contents of drawings or supplementary material, or both, the latter shall take precedence.

Siemens is not liable, for whatever legal reason, for damages or personal injury resulting from the use of the application tips.

All rights reserved. Any form of duplication or distribution, including excerpts, is only permitted with express authorization by SIEMENS.

# Text boxes

SIMATIC

S7-200 Tips

Modbus Master

RS-485 Communication

S7- 214 Modbus Slaves