611A 换控制板步骤

1.Power–up the unit――― (supply ON)

2.Does the operating display”P–000” appear？  yes 往下    no 跳到7.步（有报警的解决报警）

3. Set P–051 to 4H(remove write protection 打开写保护

4. Set P–097 to 0H(start initialization)初始化

5. Set P–052 to 1H(write into FEPROM 写入FEPROM

6. Wait until P–052 is again set to 0H,then switch the converter off and 2 s after the operating display has been canceled,  power–up again 等待2秒52自动变为0H 断电重启。

7. Display ”P–095” or ”P–096”

8. Enter and check 输入以下参数

P–095 power modulecode number

. P-096 :ENTER the motor type

P-098 :ENTER the numter of encoder pulses per motor revolution。

9. Set P–097 to 1H   ”SEtUP” is displayed

10. Wait until the operating display   P–000 appears

11.IS a special motor used，where there is no code number definded for P-096? 确认是不是西门子专用电机。

1)Yes:  enter  p-159---p-176。

set p-177 to 1 (calculate motor data) wait until p-177 is again set to 0H （可能不用这步）

Set P–051 to 4H   Set P–052 to 1H

Wait until P–052 is again set to 0H (write into FEPROM)接12

2)No 接 12

12. Check, and if required, change the following parameters:

P–014 normalization nset

P–015 offset correction nset

P–024 normalization nset

P–016 ramp–up time, ramp–fct. generator 1

P–017 ramp–down time, ramp–fct. generator 1

P–029 maximum motor speed nmaxmot

P–021 to P–023, relay response values of the

P–027 speed monitoring

P–039 to P–043 torque limits

P–047to p050

P–057 to P–058 open–controlled range

P–059 to P–060 limits

P–081 to P–089 freely–programmable

terminal functions

P–113 to P–114 speed setpoints

P–185 to P–194, freely–programmable

P–241 to P–246 Relay functions

13.值改过Set P–052 to 1H

Wait until P–052 is again set to 0H (write into FEPROM)

14. Check all parameterized functions and if required change

值改过Set P–052 to 1H

Wait until P–052 is again set to 0H (write into FEPROM)

15.Set P–051 to 0H.Set write protection

整理于   2009.9.22